## Slide 1
Seth King
NETL NRAP Reservoir workgroup overview
Research Scientist, URS
October 23, 2014

## Slide 2: Outline
Smith Analysis Group
  Building metrics of reservoir performance associated to risk
ROM development
  Components of integrated assessment models (IAMs) used to probe uncertainties
    Surrogate Reservoir Model (SRM)
    Polynomial Chaos Expansion (PCE)

## Slide 3: Smith Analysis Group General Focus/Approach
What we’re doing
  Developing a synthetic database of reservoir behavior to inform two questions:
    How does reservoir performance change as a function of injection volumes & rates?
    How does a reservoir respond as a function of time when injection stops?
What we’ve done…
  Explored behavior of a few prototype reservoirs as a function of operational and geological variables using physics-based simulations
  Used three reservoir performance metrics that relate to potential risks of concern (i.e., not a direct measure of risk)
    Size of CO2 Plume
    Size of Pressure Plume
    Change in Pressure over Time (at a Point)
  Monitored metrics using simple parameters; threshold values for pressure reflect a range from small increase through thresholds with potential to cause impact

## Slide 4: Overview of Detailed Simulations
Multiple reservoir types
  Unbound sandstone formation (regional dip), homogeneous, varying permeability
  Multilayer, domal sandstone reservoir (based on Citronelle), history matched
  Domal, sandstone & limestone (based on Rock Springs Uplift), heterogeneous, multiple injectors
Operational parameters considered
  Constant-rate injection
  Varying Injection rates (10kt to 5Mt/yr)
  Varying Injection times (3 to 30 years)
  Post Injection: Monitoring pressures and CO2 at various time points (from 20 to 200 years, based on size of injection)
Subsurface parameters considered
  Permeability; permeability ratio (kh:kv); porosity; compressibility; salinity; model domain size; formation thickness and surrounding permeability
Results based on >1000 detailed simulations
  Continuum scale reservoir simulators
  Full, 3D simulations; no chemistry; no mechanics beyond compressibility
  Simulation times hours to days

## Slide 5: Reservoirs Considered
Unbound sandstone: Regional Dip
  LBNL Team (Zhang et al.) simulated using TOUGH2 and TP3D
  General unstructured, dipping sandstone reservoir
  Runs varying specific parameters
Multi-layer, domal sandstone
  NETL Team (Fathi et al.) simulated using CMG
  Derived from Citronelle, history-match model
  Two models: detailed but small domain; generalized but larger domain
  Runs varying specific parameters
Domal, dipping sandstone-limestone
  LANL Team (Dempsey et al.) simulated using FEHM
  Derived from Rock-Springs Uplift site model
  Runs varying geologic heterogeneity & other parameters
Unbound sandstone
  LANL Team (Dempsey et al.) simulated using FEHM
  General unstructured flat sandstone aquifer
  Stochastic evaluation for specific parameters

## Slide 6: Metrics Analyzed
Size of CO2 Plume
Size of Pressure Plume
Pressure at at a Location
Size of CO2 plume injection
  Rate of growth for early phase
  Rate of growth for long-term phase
  Plume radius at end of injection
Size of pressure plume
  Maximum size of plume
  Various pressure thresholds
    Brine rise
    Fault-slip criteria
Pressure at a location
  Maximum pressure increase

## Slide 7: Growth of CO2 plume has a characteristic behavior, albeit details vary between sites.
Domal Sandstone-Limestone (10-yr injection; 1-50 Mt)
Multi-layer, Domal Sandstone (3-yr injection; 0.1-10 Mt)
Unbound Sandstone, Regional Dip (0° dip; kh=100 mD; f=0.2)
injection: rapid growth
post-injection: slow growth to stable
Unbound Sandstone, Regional Dip (0° dip; kh=1000 mD; f=0.2)

## Slide 8: Amount of CO2 injected is primary factor in the growth rate and size of CO2 plume.
Increase in mass of CO2 increases the growth rate for the CO2 plume (both early and long-term rates)
Increase in porosity decreases growth rate
Permeability has minimal impact on growth rate and small impact on size of CO2 plume
Unbound Sandstone, Regional Dip (0° dip)
Unbound Sandstone, Regional Dip (0° dip)
Unbound Sandstone, Regional Dip
(1° dip; 1Mt/yr)
operational
geological

## Slide 9: Growth of pressure plume has a characteristic behavior, albeit details vary between sites.
Domal Sandstone-Limestone
Unbound Sandstone, Regional Dip (0° dip)
injection: rapid growth
post-injection: reaches maximum size;
slow decay

## Slide 10: Amount of CO2 injected and geologic details each impact the area/distance for pressure effects.
Increase in mass of CO2 increases the distance of pressure effects for a given threshold
Decreasing permeability can significantly increase distance (or size) of pressure effects
Increasing the permeability can dramatically decrease distance (or size) of pressure effects
Unbound Sandstone, Regional Dip (0° dip)
(kh=10 mD)
Domal
Sandstone-Limestone
(kh=100 mD)
(kh=1000 mD)
operational
geological

## Slide 11: Pressure increase in reservoir has a characteristic behavior, albeit details vary between sites.
Unbound Sandstone, Regional Dip (0° dip; 1 Mt/yr)
Unbound Sandstone, Regional Dip (0° dip; @1 km)
Domal Sandstone-Limestone
injection: early rapid growth
post-injection: rapid decay
Distance
from Injector

## Slide 12: Amount of CO2 injected and geologic details each impact the magnitude of pressure increase.
Increase in mass injected increases maximum DP at a given distance from the injection well
Increase in permeability decreases maximum DP at a given distance from the injection well
Unbound Sandstone, Regional Dip (0° dip)
Unbound Sandstone, Regional Dip
(1° dip; 1 Mt/yr)
operational
geological

## Slide 13: General Observations
Two question
  How does reservoir performance change as a function of injection volumes & rates?
  How does a reservoir respond as a function of time when injection stops?
Impact of operational variables…
  Reservoir response varies with amount of injected CO2
    Size of CO2 Plume—rapid growth during injection; slower growth post injection
    Size of Pressure Plume—rapid growth during injection; reaches maximum and decays post
    Change in Pressure over Time—rapid growth during injection; rapid decline post injection
  Potential to exceed some pressure thresholds depends on size of injection
Impact of geologic variables…
  Reservoir response varies with geologic type
  Rate of CO2 plume growth depends on reservoir porosity
  Potential to exceed some pressure thresholds depends on reservoir permeability
Impact of geologic variables is on the same order as operational variables.

## Slide 14: Reservoir Analysis Toolkit (RAT)
Takes in Pressure and Saturation values output from Simulation software (modular design accommodates different file types).
Outputs plume sizes through time and pressure values in specified grid blocks at each time step.
Scriptable to process multiple realizations.
Initial GUI interface developed (needs updated since new metrics introduced).

## Slide 15: ROM Type: Surrogate Reservoir Model (SRM)
Reservoir Reduced Order Models (ROMs) for use with Integrated Assessment Models (IAMs)

## Slide 16: What is an SRM?
Above
Below
Main Grid
East
West
North
South
Grid-Based SRM uses machine learning to train, calibrate, and validate a data-driven model capable of replicating the results of fluid flow through porous media in a simulation grid cell.
The data-driven model is trained to reproduce pressure or saturation changes within a simulation grid cell as a function of:
  Reservoir Characteristics
  Imposed Physics (multi-physics)
  Operational Constraints
Applied Throughout the field

## Slide 17: Steps involved in developing SRM
Steps
  Generate a few initial simulations with full CMG reservoir model (18 simulations)
  Create database of CMG inputs and outputs for each simulation
  Select and organize data to ensure appropriate relationships between less or more distant neighbor cells are captured; generate SRM input
  Train neural networks (here using 2% of the CMG input/output tables), calibrate, and verify for each parameter of interest
  Apply neural networks to blind scenarios for testing
Different SRMs generated based on time period
  During injection
  Post-injection
Interpolation in space and time as in LUT
Spatially-varying porosity and permeability
Rate and duration of injection varied
Hidden Layer
Output Layer
Input Layer
Amini et al, 2011
Notes: No physics included; just neural networks training
There are several neural networks for one specific type of locations (grid blocks); e.g., those close to the faults, close to injector, those farther away; etc.
Step 3 is about how to organize these neural networks
Training involves developing appropriate linkages between input and output (hidden layer); non-physical

## Slide 18: Reservoir model used for SRM development
CO2 Injection
Monitoring Well
Saline Sandstone Reservoir Within Depleted Gas Field
  Based on actual CO2 injection site in southern Australia
  Simulations for moderate injection of 35,000-100,000 t CO2 over 5 years
  18 intermediate-scale CMG simulations performed with history-matched model
  Surrogate model based on artificial intelligence and data mining approach using neural networks
  Permeability and porosity vary spatially in each reservoir grid block

## Slide 19: Surrogate models compare well to reservoir simulations
CO2 Mole Fraction
psi
psi
Fraction
Fraction
50 years after Injection

## Slide 20: Second reservoir model for SRM development
Saline Sandstone Reservoir Within Depleted Gas Field
  Based on actual EOR field in West Texas (40 years of CO2 injection)
  Upscaled porosity and permeability model (Han et al, 2008)
  10 CMG simulations with history-matched model, begin after oil production completed
  Allow injection for 50 years in several wells at a given wellhead pressure
  Permeability and porosity vary spatially in each reservoir grid block
Porosity
Permeability

## Slide 21
Start of Simulation
Start of Injection
01/01/2172
2172
End of Injection
01/01/2222
2222
3172
9 yrs after Injection
01/01/2181
Simulator (CMG) Results
SRM (GRNN) Results
% Relative Error
Surrogate models compare well to reservoir simulations

## Slide 22: Summary for SRM technique
Type of reservoirs: Gas field, sandstone, moderate-high complexity
          Oil field, sandstone, moderate complexity, many wells
ROM properties:
  Requires few reservoir simulation runs (<15-20)
  Good accuracy w.r.t. reservoir simulation (<5-10% error in 95-99% of cases)
  Allows for spatial heterogeneity variability
  Allows for operational variability (e.g., rate of injection, length of injection, bottomhole pressure)
  Fast run time (~1 min for 10,000 grid blocks; ~10s for ~1,000 grid blocks)
  Takes time to train SRM once reservoir simulation runs are complete (months; speed improves with practice)
  SRM based on data collected post injection may not need any re-training, just updating of reservoir parameters used, if data is within envelope of predictions of initial SRMs

## Slide 23: ROM Type: Polynomial Chaos Expansion (PCE)

## Slide 24: What is the PCE technique?
Input
Output
permeability, porosity, etc
pressure,
gas saturation, etc
Polynomial Chaos Expansions:
Numerical Simulation
Spatially varied porosity and permeability
Used porosity and permeability in 6 nearest grid blocks for predictions
Varied bottomhole pressure in wells
Spatial and temporal discretization and interpolation as in LUT and SRM

## Slide 25: PCE technique uses mixed integer programming
Initialization at degree d = 0
Sample
d = d + 1
Solve a mixed-integer problem (MIP) for a best subset of bases functions
Overfitting?
Stop
Errord small?
Yes
No
degree d
Terms T
R2
Cross validation
Accuracy
d*, T*
1
Underfitting
Overfitting
Novelty of proposed PCE method:
Computationally efficient
Obtains simpler models

## Slide 26: Used same field for PCE and SRM
Saline Sandstone Reservoir Within Depleted Gas Field
  Based on actual EOR field in West Texas (40 years of CO2 injection)
  Upscaled porosity and permeability model, 35x26 grid (Han et al, 2008)
  10 CMG simulations with history-matched model, begin after oil production completed
  Allow injection for 50 years in several wells at a given wellhead pressure
  Permeability and porosity vary spatially in each reservoir grid block
Porosity
Permeability

## Slide 27: Summary for PCE Method
Type of reservoir: Oil field, sandstone, moderate complexity, many wells
ROM properties:
  Fast run times (~1s for ~1,000 grid blocks)
  Used ~10-20 simulation runs (may require more runs to improve accuracy; sampling methods can help select runs needed)
  Construction once reservoir simulation runs is relatively fast with MIP technique (1-2 weeks)
  Allows for some operational parameter variability
  Updating LUT based on data collected post injection requires re-running reservoir simulations and generating new ROMs
  Questionable accuracy w.r.t. reservoir simulation for parameter combinations not explicitly trained for; issues with spatial heterogeneity or reservoir properties; did work well on a 2-D test case with homogeneous properties (<6% error)

## Slide 28: Summary of ROM Approaches
The three types of ROMs each have their own distinct characteristics
  Run time
  Number of reservoir simulations needed
  ROM development/training time
  Flexibility
  Accuracy
Different ROMs may be more suited for different applications or stages of a project:
  LUT suitable for site characterization phase with large parameter uncertainty with highly unknown reservoir parameters
  SRMs suitable for later project stage with partial history matching and uncertainty mainly in future injection rates and heterogeneous structure
  PCE applicability similar to LUT with some additional flexibility for a larger number of input parameters, potentially spatially varying